Le strum / The information on this page is the bare minimum needed to build the project, however you will find expanded information for building LE STRUM at the following URL https://github.com/hotchk155/Voici-Le-Strum/wiki / LE STRUM Component Designators / R1, R2 - 220 Ohm (red-red-brown code) resistor / R4, R8 - 1 kOhm (brown-black-red code) resistor / R3, R5, R6, R7 - 10 kOhm (brown-black-orange code) resistor / C1, C2, C3, C4, C7 - 100nF Ceramic Capacitor (104 code) / C5, C6 – 4u7 electrolytic capacitor / D1- 1N4001 Rectifier Diode / D2 – D17 - 1N4148 Small Signal Diode (x16) / REG1 - +5V 100mA Regulator TO92 / MIDI, PWR - 3mm LED / Solder the IC sockets before fitting IC's. Check orientation of pin 1 notch/dimple with markings on PCB) / IC1 - PIC16F1825 Microcontroller with LE STRUM firmware, fitted into 14 pin DIP IC socket / IC2, IC3 - 74HC595 Shift Register, fitted into 16 pin DIP IC socket / S1-S37 - 6mm Momentary Tactile Switch (x37) / ONOFF - Miniature slide switch / MIDI_OUT - 5 PIN DIN socket PCB mount / ICSP - 6 way SIL right angle pin header (optional) / BAT1 - PP3 Battery Box / STYLUS - 4mm Banana Plug on wire / Switches, Battery holder + M2.5 nuts/bolts, Standoff Pillars + M3 bolts – it should be reasonably obvious where all those bits go but if in any doubt please refer to the detailed build instructions at the URL given above. / I hope you enjoy LE STRUM. If you have any problems please contact me at the following email sixtyfourpixels@gmail.com or via the site where you ordered LE STRUM / LE STRUM is an open source, open hardware project. All input is welcome, from wish-list ideas to actual code and hardware hacks and mods. / Cheers / Jason Hotchk155	Le strum / The information on this page is the bare minimum needed to build the project, however you will find expanded information for building LE STRUM at the following URL https://github.com/hotchk155/Voici-Le-Strum/wiki / LE STRUM Component Designators / R1, R2 - 220 Ohm (red-red-brown code) resistor / R4, R8 - 1 kOhm (brown-black-red code) resistor / R3, R5, R6, R7 - 10 kOhm (brown-black-orange code) resistor / C1, C2, C3, C4, C7 - 100nF Ceramic Capacitor (104 code) / C5, C6 – 4u7 electrolytic capacitor / D1- 1N4001 Rectifier Diode / D2 – D17 - 1N4148 Small Signal Diode (x16) / REG1 - +5V 100mA Regulator TO92 / MIDI, PWR - 3mm LED / Solder the IC sockets before fitting IC's. Check orientation of pin 1 notch/dimple with markings on PCB) / IC1 - PIC16F1825 Microcontroller with LE STRUM firmware, fitted into 14 pin DIP IC socket / IC2, IC3 - 74HC595 Shift Register, fitted into 16 pin DIP IC socket / S1-S37 - 6mm Momentary Tactile Switch (x37) / ONOFF - Miniature slide switch / MIDI_OUT - 5 PIN DIN socket PCB mount / ICSP - 6 way SIL right angle pin header (optional) / BAT1 - PP3 Battery Box / STYLUS - 4mm Banana Plug on wire / Switches, Battery holder + M2.5 nuts/bolts, Standoff Pillars + M3 bolts – it should be reasonably obvious where all those bits go but if in any doubt please refer to the detailed build instructions at the URL given above. / I hope you enjoy LE STRUM. If you have any problems please contact me at the following email sixtyfourpixels@gmail.com or via the site where you ordered LE STRUM / LE STRUM is an open source, open hardware project. All input is welcome, from wish-list ideas to actual code and hardware hacks and mods. / Cheers / Jason Hotchk155