Preset Patch / (Hold MODE Button)	Command / (Hold MODE Button)	Toggle Setting (Hold MODE Button) / Single blink OFF, Double blink ON	LE STRUM QUICK REF V1.1
C C# D D# E F F# G G# A A# B / MAJ Basic / Strum / Mode Guitar / Strum / Mode Guitar / Sustain / Mode Organ Buttons / Mode Organ / Buttons / with Adds Organ Buttons with Adds/Retrig MIDI Panic (All Notes Off) / MIN Play Note / On Contact Make Play Note / On Contact Break Guitar / Open Chord / Voicing Added Notes (Sus4/6/9) Sustain Chord Until Next Chord Chromatic Scale On Pads Enable Organ Buttons On MIDI Ch 2 Sustain O/B Until Next Chord Save User Patch To / EEPROM / DOM7 Damp Note / On Contact Make Damp Note / On Contact Break Repeat Guitar Chord At / +1 Octave Map Guitar Chord Bass Notes Common Notes Sustain On Change Diatonic / Scale On Pads Pentatonic / Scale On Pads Common Notes Sustain On O/B Load User Patch From / EEPROM / C C# D D# E F F# G G# A A# B / Special Chord Button Combinations / MAJ + DOM7 = Major Seventh Chord / MIN + DOM7 = Minor Seventh Chord / MAJ + MIN = Diminished Triad / MAJ + MIN + DOM7 = Augmented Triad Added Notes (When enabled by Mode) / Hold chord and press top row button to right = Sus 4 / Hold chord and press middle row button to right = Add 6 / Hold chord and press bottom row button to right = Add 2/9 Use of the MODE button / Hold MODE and touch a pad with the stylus to set MIDI velocity / Hold MODE at startup to view firmware version

Preset Patch / (Hold MODE Button)	Command / (Hold MODE Button)	Toggle Setting (Hold MODE Button) / Single blink OFF, Double blink ON	LE STRUM QUICK REF V1.1
C C# D D# E F F# G G# A A# B / MAJ Basic / Strum / Mode Guitar / Strum / Mode Guitar / Sustain / Mode Organ Buttons / Mode Organ / Buttons / with Adds Organ Buttons with Adds/Retrig MIDI Panic (All Notes Off) / MIN Play Note / On Contact Make Play Note / On Contact Break Guitar / Open Chord / Voicing Added Notes (Sus4/6/9) Sustain Chord Until Next Chord Chromatic Scale On Pads Enable Organ Buttons On MIDI Ch 2 Sustain O/B Until Next Chord Save User Patch To / EEPROM / DOM7 Damp Note / On Contact Make Damp Note / On Contact Break Repeat Guitar Chord At / +1 Octave Map Guitar Chord Bass Notes Common Notes Sustain On Change Diatonic / Scale On Pads Pentatonic / Scale On Pads Common Notes Sustain On O/B Load User Patch From / EEPROM / C C# D D# E F F# G G# A A# B / Special Chord Button Combinations / MAJ + DOM7 = Major Seventh Chord / MIN + DOM7 = Minor Seventh Chord / MAJ + MIN = Diminished Triad / MAJ + MIN + DOM7 = Augmented Triad Added Notes (When enabled by Mode) / Hold chord and press top row button to right = Sus 4 / Hold chord and press middle row button to right = Add 6 / Hold chord and press bottom row button to right = Add 2/9 Use of the MODE button / Hold MODE and touch a pad with the stylus to set MIDI velocity / Hold MODE at startup to view firmware version