Preset Patch / (Hold MODE Button)	Command / (Hold MODE Button)	Toggle Setting (Hold MODE Button) / Single blink OFF, Double blink ON	LE STRUM QUICK REF V1.2
C C# D D# E F F# G G# A A# B / MAJ Basic / Strum / Mode Guitar / Strum / Mode Guitar / Sustain / Mode Organ Buttons / Mode Organ / Buttons / with Adds Organ Buttons with Adds/Retrig Toggle Strum Direction Load User Patch From / EEPROM / MIN Play Note / On Contact Make Play Note / On Contact Break Guitar / Open Chord / Voicing Added Notes (Sus4/6/9) Sustain Chord Until Next Chord Chromatic Scale On Pads Enable Organ Buttons On MIDI Ch 2 Sustain O/B Until Next Chord Save User Patch To / EEPROM / DOM7 Damp Note / On Contact Make Damp Note / On Contact Break Repeat Guitar Chord At / +1 Octave Map Guitar Chord Bass Notes Common Notes Sustain On Change Diatonic / Scale On Pads Pentatonic / Scale On Pads Common Notes Sustain On O/B MIDI Panic (All Notes Off) / C C# D D# E F F# G G# A A# B / Special Chord Button Combinations / ● MAJ + DOM7 = Major Seventh Chord / ● MIN + DOM7 = Minor Seventh Chord / ● MAJ + MIN = Diminished Triad / ● MAJ + MIN + DOM7 = Augmented Triad Added Notes (When enabled by Mode) / ● Hold chord and press top row button to right = Sus 4 / ● Hold chord and press middle row button to right = Add 6 / ● Hold chord and press bottom row button to right = Add 2/9 ● Hold MODE and touch a pad with the stylus to set MIDI velocity / ● Hold MODE at startup to view firmware version. LED flashes major version digit, short blink, minor version digit, short blink / ● Strum output on MIDI channel 1 at controllable velocity / ● Organ button output on MIDI channel 2 at full velocity

Preset Patch / (Hold MODE Button)	Command / (Hold MODE Button)	Toggle Setting (Hold MODE Button) / Single blink OFF, Double blink ON	LE STRUM QUICK REF V1.2
C C# D D# E F F# G G# A A# B / MAJ Basic / Strum / Mode Guitar / Strum / Mode Guitar / Sustain / Mode Organ Buttons / Mode Organ / Buttons / with Adds Organ Buttons with Adds/Retrig Toggle Strum Direction Load User Patch From / EEPROM / MIN Play Note / On Contact Make Play Note / On Contact Break Guitar / Open Chord / Voicing Added Notes (Sus4/6/9) Sustain Chord Until Next Chord Chromatic Scale On Pads Enable Organ Buttons On MIDI Ch 2 Sustain O/B Until Next Chord Save User Patch To / EEPROM / DOM7 Damp Note / On Contact Make Damp Note / On Contact Break Repeat Guitar Chord At / +1 Octave Map Guitar Chord Bass Notes Common Notes Sustain On Change Diatonic / Scale On Pads Pentatonic / Scale On Pads Common Notes Sustain On O/B MIDI Panic (All Notes Off) / C C# D D# E F F# G G# A A# B / Special Chord Button Combinations / ● MAJ + DOM7 = Major Seventh Chord / ● MIN + DOM7 = Minor Seventh Chord / ● MAJ + MIN = Diminished Triad / ● MAJ + MIN + DOM7 = Augmented Triad Added Notes (When enabled by Mode) / ● Hold chord and press top row button to right = Sus 4 / ● Hold chord and press middle row button to right = Add 6 / ● Hold chord and press bottom row button to right = Add 2/9 ● Hold MODE and touch a pad with the stylus to set MIDI velocity / ● Hold MODE at startup to view firmware version. LED flashes major version digit, short blink, minor version digit, short blink / ● Strum output on MIDI channel 1 at controllable velocity / ● Organ button output on MIDI channel 2 at full velocity